## Slide 1: RFDump: An Architecture for Monitoring the Wireless Ether
Kaushik Lakshminarayanan
Samir Sapra
Srinivasan Seshan
Peter Steenkiste
Carnegie Mellon University

## Slide 2: Popularity causes crowding
Wireless – 2.4 GHz ISM band – Unlicensed
  802.11, Bluetooth, ZigBee, Microwave oven
Packet
ACK
Packet
How do we troubleshoot such problems?
Packet
Packet
Packet

## Slide 3: How do existing sniffers work?
Tcpdump, Ethereal
Wired networks
Physical
Data Link
Network
Transport
Session
Presentation
Application
Sniffers
802.11+BT+microwave+..
Data Link
Network
Transport
Session
Presentation
Application
?
How do we bootstrap in wireless?
NIC
802.11 PHY
802.11 MAC
Network
Transport
Session
Presentation
Application
tcpdump
802.11 NIC

## Slide 4: Multi-dongle approach
Cumbersome
Sniffers don’t expose physical layer information
Don’t capture inter-protocol interactions
ZigBee
Bluetooth
802.11
How do we enable such fine-grained analysis?
802.11 PHY
802.11 MAC
Network
Transport
Session
Presentation
Application
tcpdump
802.11 NIC
BT PHY
BT MAC
Network
Transport
Session
Presentation
Application
hcidump
BluetoothNIC

## Slide 5: Software-Defined Radio (SDR): An enabler
SDR Hardware
Software
Analog signal
Exposes physical layer information
Samples
Supports programmable analysis modules

## Slide 6: SDR: Challenges
SDR Hardware
Software
Analog signal
Samples
How do we process 256 Mbps of information?
How to differentiate between samples?
Real-time
Multi-protocol, Extensibility
ZigBee, Bluetooth, 802.11 or Noise

## Slide 7: Outline
Motivation
Design of RFDump
Implementation
Evaluation

## Slide 8: A naïve solution: Demodulate all
… demodulator
Bluetooth demodulator
802.11 demodulator
ZigBee demodulator
SDR
Protocol Extensible
Real-time
  Demodulation is costly
  All demodulators process everything!
  How to make it more efficient?
ZigBee
802.11
Bluetooth
Noise
SDR
802.11 demodulator
ZigBee demodulator
Bluetooth demodulator
… demodulator
Demodulator | CPU time
802.11b 1Mbps | 0.6x
Bluetooth | 0.7x
}
5 demodulators  3x

## Slide 9: A better solution: Energy filter
Demodulators do less work
  Only when medium utilization is very low
What if medium utilization is very high
  Real-time
Need fast demultiplexing
SDR
802.11 demodulator
ZigBee demodulator
Bluetooth demodulator
… demodulator
Energy
Filter
ZigBee
802.11
Bluetooth
Noise

## Slide 10: RFDump: High-level idea
Fast detector – map signal to protocol
  Protocol extensible
  Real-time
Detectors can be faster
  Can tolerate false positives
  Can tolerate delay
ZigBee
802.11
Bluetooth
Noise
SDR
802.11 demodulator
ZigBee demodulator
Bluetooth demodulator
… demodulator
Energy
Filter
Fast detector

## Slide 11: How do we detect protocols?
Packet
MAC-level ACK
SIFS
Time
Timing
  802.11 – Interframe Space (SIFS, DIFS)
  Bluetooth – TDD slots
Phase
  802.11b 1Mbps – DBPSK
  Bluetooth – GMSK
Frequency (Channel width)
  802.11b – 22 MHz
  Bluetooth – 1 MHz
Packet
MAC-level ACK
SIFS
Time
I
Q
I
Q
Frequency
802.11b
Bluetooth
22 MHz
1 MHz
Constellation
diagram

## Slide 12: How to make detection fast?
Detection stage
Protocol-agnostic
Protocol-specific
Peak detector
802.11
SIFS/DIFS
Bluetooth
Slot time
ZigBee
Slot time
Light-weight
5% real-time
Metadata
(coarse)
Start and end of frames
Samples
(fine)

## Slide 13: RFDump: Putting the pieces together
Fast detector
SDR
Energy
Filter
802.11 demodulator
ZigBee demodulator
Bluetooth demodulator
… demodulator
Energy
Filter
SDR
802.11b
(1 Mbps)
demodulator
Bluetooth demodulator
Peak detector
802.11 SIFS/DIFS
Bluetooth TDD Slot
QPSK
DBPSK
802.11b
(1 Mbps)
Filter
BT Filter
In-depth
analysis stage
GFSK
ZigBee Slot time
802.11b
(2 Mbps)
demodulator
ZigBee
demodulator
802.11b
(2 Mbps)
Filter
ZigBee
Filter
SDR
Energy
Filter
Yes
Yes
M
Detection stage
Protocol-specific
Protocol-agnostic
Timing Analysis
Phase Analysis

## Slide 14: Implementation
GNU Radio and USRP SDR platform
Fast detectors – 802.11b (1 Mbps) and Bluetooth
Limited by USRP1 8MHz bandwidth

## Slide 15: Evaluation
  Are the detectors accurate?
  Microbenchmarks (CMU wireless emulator)
Do they have false positives?
  Traffic mix (CMU wireless emulator)
Are the detectors fast?
  Different loads

## Slide 16: Bluetooth detection accuracy
6000 L2CAP pings between 2 Bluetooth nodes
Very accurate at high SNRs
Accurate at low SNRs
Good region
SNR (dB)
Packet Miss
Rate

## Slide 17: Traffic mix detection accuracy
Bluetooth and 802.11b 1 Mbps (1000 packets)
Detector | Packet miss rate (%) |  | False positive rate (%) | 
 | 802.11b | Bluetooth | 802.11b | Bluetooth
Timing | 1.8 | 2.4 | 0.07 | 0.7
Phase | 1.8 | 1.2 | 1 | 0.2
Low packet miss rate
Low false positive rate

## Slide 18: How fast is detection?
8 demodulators for Bluetooth, 1 for 802.11
Fast detection even at high loads
Good region
Medium Utilization (%)
CPU time
Real time

## Slide 19: Related work
802.11 connectivity diagnosis
  ClientConduit (Mobicom ‘04), WiFiProfiler (MobiSys ‘06)
802.11 performance diagnosis (Enterprise networks)
  Jigsaw (SIGCOMM ‘06, 07), Wit (SIGCOMM ‘06), DAIR (NSDI ’07)
  MOJO (MobiSys ‘06)
Detection
  Many – recently, WhiteFi (SIGCOMM ‘09)
SDR Performance
  Sora (NSDI ‘09), Split-functionality approach (NSDI ‘09)

## Slide 20: Summary
Wireless is ubiquitous
Hard to diagnose protocol/device interactions
Built RFDump tool for monitoring
  Efficient (light-weight detection modules)
  Accurate
  Extensible (SDR)
  Scalable (protocol-agnostic detection modules)

## Slide 21: Future Work
Extend to USRP 2 to overcome the limitations of USRP 1
Wireless Diagnosis
  Interference detection
  Interference cancellation
Dynamic Spectrum Access

## Slide 22: Timing vs Phase
Phase analysis
  More accurate at high SNRs
  More expensive than timing
  Cannot detect when collisions easily
Timing analysis
  More accurate at low SNRs
  Very light weight
  Cannot detect 802.11 broadcast packets in low contention
  Can use signal strength to detect collisions

## Slide 23: OFDM
Could not experiment due to 8 MHz constraint
Mix of frequency and phase/amplitude
  Subcarriers
  Modulation scheme

## Slide 24: Evaluation - Accuracy
802.11b Microbenchmark (Wireless Emulator)